## Slide 1: SPI Slave Design
BY Eric Yang 2026.08

## Slide 2: Overview
Features
  CPOL=0, CPHA=0
  MSB first
  Back-to-back transfer support
  8 x 16-bit registers available
  Read data within the same frame
  No system clock
  24-bit self-defined frame protocol
Frame Structure (MSB first)
  [23] RW 0 = write, 1 = read
  [22:16] ADDR only the low AW bits are decoded, upper bits ignored
  [15:0] DATA
Easy to communicate with MCU using an 8-bit SPI peripheral.
3 Back-to-back transfers per frame with software NSS control.

## Slide 3: Front-end Design
SPI Slave Block Diagram
No system clock:
- No CDC problem
Design is parameterized –
Easy to customize the frame format,
or modify the number of registers.

## Slide 4: RTL Simulation
Simulator: VCS
Testbench Language: SystemVerilog
Verification tasks:
  Reset behavior
  All zeros/ones transfer
  Back-to-back transfer
  Read/Write same addr
  Read/Write when deselected
  Randomized multi-frame transfer
  Functional coverage

## Slide 5: Coverage Report
Functional Coverage
  Cover both read and write
  Cover all 8 regs
  Cover arbitrary addr_hi
  Cover data with boundary conditions
  (Cross Cover) All regs should be both read and written
Line/Cond/Toggle/Branch Coverage
  All 100% in VCS coverage report

## Slide 6: Waveforms of Transfers
Write 16’hABCD to 7’d3
Write 16’h2FAE to 7’d6
Read from 7’d6
Read Command
Data Received
Back-to-back transfer

## Slide 7: Back-end Design
Constraints (Without IO)
  Clock Frequency: 10MHz
  Clock Uncertainty: ~10% T
  Clock Transition: 0.3ns
  Duty Cycle 60% (60% High, 40% Low)
  Input/Output delay:
    Max (setup): Assume 50% CLK_LOW for setup
    Min (hold): No requirement as a half-cycle remains before sampling
  Max Fanout: 20
Data is transmitted at negedge,
but sampled at posedge.
Critical path for output delay (setup).

## Slide 8: DC & FM
DC Summary
  No Violation
  Area: 12014.33 um2
FM Summary
  No LAT
  Verification Succeeded

## Slide 9: Innovus
Process: TSMC 0.18um
LIB: tcb018gbwp7t
  WC: SS/125℃/1.62V for setup
  BC: FF/ 0℃ / 1.98V for hold
FloorPlan
  Die: 294um * 98um
    DIE_W = 294 = core 270 + 2 x 12 margin
    DIE_H = 98 = core 80 + 2 x 9 margin
  Pins: {miso miso_oen mosi sck ssn rst_n}

## Slide 10: Innovus
Power
  Power Ring
    Metal 6 Vertical
    Metal 5 Horizontal
  Power Stripe
    Metal 6 Vertical
    4 sets
  Power Rail
    Metal 1 Horizontal

## Slide 11: Innovus
Summary
  Density: 67.928%
    100.000% with Fillers
  Total number of glitch violations: 0

## Slide 12: IO Plan
Power IO
  Pre-drivers & Core
    1.8V
  Post-drivers
    3.3V
    We take PVDD2POC as the
    post-driver power supply
  Power On Control
    Will explain later

## Slide 13: IO Plan
Digital IO
  Input (PRXW0812SCDG)
    Pull-up: rst_n, ssn
    Pull-down: sck, mosi
    Schmitt Trigger Input
      For noise immunity
  Output
    PRDW0812SCDG
    With Slew Rate Controlled Output
      Reduce peak current
    8mA output
      ~7ns edge @20pF, 3.3V

## Slide 14: Virtuoso Layout
My Part

## Slide 15: Virtuoso Layout

## Slide 16: LVS & DRC
LVS
  All passed
DRC
  UTM40K.R.1 { @ Min. density of M6 area >= 30% }
    Dummy fill by others
  PO.R.3 { @ Min poly area coverage < 14% }
    Dummy fill by others
  M5.R.1 { @ Min M5 area coverage < 30%}
    Dummy fill by others
  ESD.24g & ESD.25g
    Waived due to rn_tpd018nv_280a.pdf

## Slide 17: Gate-level Simulation
Simulator: VCS
Testbench Language: SystemVerilog
Same tasks with SDF annotation
Max/Min all passed

## Slide 18: Post-layout Simulation
POC test
Why POC?
  The power-up sequence between rails is not guaranteed
  It is common for the IO supply (3.3 V) to come up before the core supply (1.8 V)
  POC is required to clamp the IO into a known state (typically high-Z) until the core supply is stable

## Slide 19: POC Test
How to test high-Z:
  Connect IO to 1.65V with 1M resistor
  If pad is high-Z,
  it’ll be clamped at 1.65V
  If pad is controlled by the core,
  it’ll be either near 3.3V / 0V

## Slide 20
50us late for VDD
POC cutoff
PAD is controlled by core
POC on
ssn rst_n high
sck mosi low
miso high-Z
Controlled by POC
POC cutoff
State switch
VDD is not large enough to turn off
VDDPST-PMOS-NMOS-GND
Current rises
Level shifter on
Current off
Level shifter on Switching current
POC Test @ tt/1.8V/3.3V/27°C

## Slide 21: Critical Timings
tEN: Output enable time
  Maximum delay from the falling edge of ssn until miso leaves the high-Z state and is actively driven
  Measured from the 50% point of the ssn waveform to the 50% point of the miso waveform

## Slide 22
tEN = 6.02ns @ ss/1.62V/3.0V/125℃, CL=20pF

## Slide 23: Critical Timings
tDIS: Output disable time
  Maximum delay from the rising edge of ssn until miso returns to the high-Z state
  Measured the current from stable to approximately 0
    Time for miso to return to high-Z voltage is determined by the external R and CL
miso active
current
miso high-Z
current

## Slide 24
tDIS = 2.64ns @ ss/1.62V/3.0V/125℃, CL=20pF

## Slide 25: Critical Timings
tV: Data output valid time
  Maximum delay from the falling edge of sck to miso becoming valid
  Measured from the 50% point of the sck waveform to the 50% point of the miso waveform

## Slide 26
tV = 6.26ns @ ss/1.62V/3.0V/125℃, CL=20pF

## Slide 27: AMS Simulation
Write an SPI Master in SystemVerilog
Connect to SPI Slave
Run AMS to check the transfer waveforms

## Slide 28
AMS Simulation Passed @ ss/1.62V/3.0V/125℃, CL=20pF

## Slide 29: ELECTRICAL CHARACTERISTICS
PARAMETER | SYMBOL | DESCRIPTION | SPEC |  |  | UNIT
 |  |  | MIN | TYP | MAX | 
IO Supply | VDDPST |  | 3.0 | 3.3 | 3.6 | V
Core Supply | VDD |  | 1.62 | 1.8 | 1.98 | V
Power-on Current | Ipk |  |  | 0.1 | 6 | mA
Load Capacitance | CL |  |  | 20 |  | pF
Clock Period | tSCK |  |  | 100 |  | ns
ssn Setup/Hold Time | tSSH /tSSN | Innovus STA & testbench verified |  | 10 |  | ns
Minimum ssn High Time | tIDLE | Innovus STA & testbench verified |  | 10 |  | ns
Output Enable Time | tEN | ss/1.62V/3.0V/125℃, 20pF |  |  | 7 | ns
Output Disable Time | tDIS | ss/1.62V/3.0V/125℃, 20pF |  |  | 3 | ns
Data Output Valid Time | tV | ss/1.62V/3.0V/125℃, 20pF |  |  | 7 | ns

## Slide 30: MISC
Resistor/Diode mismatches in IO library have all been fixed,
all IOs in the library are now available
All scripts are included in tsmc18/Digital/README
Check my smb_share to use the updated version

## Slide 31
Thanks!